## Slide 1
An Automated Hardware/Software Co-Design Flow for Partially Reconfigurable FPGAs
Kostas Andronikos
AEM : 9754

## Slide 2
Topics
DAPR
Introduction
Evaluation and Results
HW/SW PR Partitioning
PR Floorplanning
1
2
3
4
5

## Slide 3: Introduction
Idea
  Partial reconfiguration is a technique that allows for the dynamic modification of a portion of the FPGA
Benefits
  Reduced HW, Power, Memory Requirements
  Tasks can be executed on SW processors and/or in the HW PRRs
Challenges
  Complex Design

## Slide 4: Introduction
HW/SW Design Flow
  HW/SW PR Partitioning
    HW/SW Partitioning, which makes a high-level mapping of tasks into SW and/or HW
    PR Partitioning, which locates the HW tasks into one or multiple PRRs
  PR Floorplanning
    PRR Floorplanning, which sets the physical placements of the PRRs on the FPGA fabric
    Partition Pin Floorplanning, which sets the physical placements of the hardware communication interfaces or partition pins
  Bitstream and Binary Executable Generation
Notes: PRR floorplanning sets the physical placements of the PRRs on the FPGA fabric.
Partition pin floorplanning sets the physical placements of the specialized hardwired communication interfaces or partition pins, on PRR boundaries

## Slide 5: DAPR
  Necessity
    Applications have a very large number of functionally-equivalent HW/SW PR partitions with different resource and reconfiguration time tradeoffs
    Required lengthy design exploration time for evaluation of all these different partition options
  Benefits
    Reduction of the required time for evaluating the different partitioning options
    Eliminates the need for designers to be familiar with low-level FPGA details and complexities, so reduces manual design effort.

## Slide 6: DAPR
Design Flow
  Takes as input a modularized application and generate input parameters for HW/SW PR Partitioning
  The HW/SW PR generates a set of functionally-equivalent HW/SW PR partitions with associated total resource requirements, reconfiguration times and execution times
  The designer analyzes this set and chooses the most suitable partition
  The PR Floorplanning improves the clock frequency
  Bitstreams and Binary executables are generated

## Slide 7: HW/SW PR Partitioning
Performance
  For a PR Design with 16 tasks the algorithm detected all the possible partitions in 5 minutes when running on an Intel Core 7 2.5GHz CPU with 8GB RAM
HW/SW PR Partitioning Algorithm

## Slide 8: PR Floorplanning
PR Floorplanning Algorithm
If the clock frequency requirements are not met the candidate floorplan is updated

## Slide 9: Evaluation and Results
Experimental Set up
  JPEG CODEC experiments executed on a PC with an Intel® Core ™ 7 2.5 GHz CPU with 8 GB of RAM.
Notes: As mentioned earlier, once the base station receives the data , it is subsequently transferred to the TelemetryDrive app through a serial communication channel, since the app operates on a computer.

## Slide 10: Evaluation and Results
The input parameters for the HW/SW Partitioning
Notes: The table 1 are the input parameters for the HW/SW PR design partitioning

## Slide 11: Evaluation and Results

## Slide 12: Evaluation and Results

## Slide 13: Evaluation and Results

## Slide 14
Thank you for your attention